## Slide 1: LLVM Bugzilla 5615, and fun with Alignment Zia Ansari Principal Engineer MCC/DPD/SSG 4/22/15

## Slide 2: 5615 Description
Hot spot of loop:
Input is series of predictable values (12341234… for example)
Performance varies based on how function is aligned
  CQ is very old, and it’s unclear on which architecture the tests were run
  On IVB and HSW perf swings 50%-70% depending on alignment of loop
static int interpret_switch(Opcodes opcodes) {
int result = 0;
while (true) {
switch (*opcodes++) {
case RETURN: return result;
case INCREMENT: result++; break;
case DECREMENT: result--; break;
case DOUBLE: result <<= 1; break;
case SWAPWORD: result = (result << 16) | (result >> 16); break;
}
}
}

## Slide 3: 5615 Let’s Pick 2 Alignments
Head of routine aligned on 0 MOD 16 byte boundary
0 mod 32
400ba0: xor %eax,%eax
400ba2: jmp 400ba6
400ba4: inc %eax
400ba6: movzbl (%rdi),%ecx
400ba9: inc %rdi
400bac: cmp $0x4,%rcx
400bb0: ja 400ba6
400bb2: jmpq *0x400ec0(,%rcx,8)
400bb9: dec %eax
400bbb: jmp 400ba6
400bbd: add %eax,%eax
400bbf: jmp 400ba6
400bc1: mov %eax,%ecx
400bc3: shl $0x10,%ecx
400bc6: sar $0x10,%eax
400bc9: or %ecx,%eax
400bcb: jmp 400ba6
400bcd: retq
16 MOD 32
400bb0: xor %eax,%eax
400bb2: jmp 400bb6
400bb4: inc %eax
400bb6: movzbl (%rdi),%ecx
400bb9: inc %rdi
400bbc: cmp $0x4,%rcx
400bc0: ja 400bb6
400bc2: jmpq *0x400ed0(,%rcx,8)
400bc9: dec %eax
400bcb: jmp 400bb6
400bcd: add %eax,%eax
400bcf: jmp 400bb6
400bd1: mov %eax,%ecx
400bd3: shl $0x10,%ecx
400bd6: sar $0x10,%eax
400bd9: or %ecx,%eax
400bdb: jmp 400bb6
400bdd: retq
~50% faster!

## Slide 4: How Does the DSB Work
DSB = Decoded Icache
  Takes decoded uops and stores them in a cache to avoid re-fetch/decode
  Increases FE throughput by delivering larger # of uops
1
2
3
4
5
31
32
.
.
.
.
.
.
1
2
8
32 Sets
8 Ways
6 UOPS Per Way
1
2
3
4
5
6
Each way contains uops from 1 32B chunk of instructions
Only 3 ways are permitted to map to the same 32B chunk
JMP uop ends a way
LSD kicks in only if all UOPs of a loop are in the DSB
  Loop stream detector
  Maximum throughput.. No fetches or DSB hits
Look under “Decoded Icache in:
http://www.intel.com/content/www/us/en/architecture-and-technology/64-ia-32-architectures-optimization-manual.html

## Slide 5: Let’s Look at the Fast Case
0 mod 32
1) 400ba0: xor %eax,%eax
2) 400ba2: jmp 400ba6
3) 400ba4: inc %eax
4) 400ba6: movzbl (%rdi),%ecx
5) 400ba9: inc %rdi
6) 400bac: cmp $0x4,%rcx
6) 400bb0: ja 400ba6
7) 400bb2: jmpq *0x400ec0(,%rcx,8)
8) 400bb9: dec %eax
9) 400bbb: jmp 400ba6
10) 400bbd: add %eax,%eax
11) 400bbf: jmp 400ba6
12) 400bc1: mov %eax,%ecx
13) 400bc3: shl $0x10,%ecx
14) 400bc6: sar $0x10,%eax
15) 400bc9: or %ecx,%eax
16) 400bcb: jmp 400ba6
17) 400bcd: retq
Set A
way 1
3 | 4 | 5 | 6 | 7 | 
way 2
8 | 9 |  |  |  | 
way 3
10 | 11 |  |  |  | 
Set B
12 | 13 | 14 | 15 | 16 | 
way 1

## Slide 6: Now Let’s Look at the Slow Case
16 MOD 32
1) 400bb0: xor %eax,%eax
2) 400bb2: jmp 400bb6
3) 400bb4: inc %eax
4) 400bb6: movzbl (%rdi),%ecx
5) 400bb9: inc %rdi
6) 400bbc: cmp $0x4,%rcx
6) 400bc0: ja 400bb6
7) 400bc2: jmpq *0x400ed0(,%rcx,8)
8) 400bc9: dec %eax
9) 400bcb: jmp 400bb6
10) 400bcd: add %eax,%eax
11) 400bcf: jmp 400bb6
12) 400bd1: mov %eax,%ecx
13) 400bd3: shl $0x10,%ecx
14) 400bd6: sar $0x10,%eax
15) 400bd9: or %ecx,%eax
16) 400bdb: jmp 400bb6
17) 400bdd: retq
Set A
way 1
3 | 4 | 5 | 6 |  | 
way 2
8 | 9 |  |  |  | 
way 3
10 | 11 |  |  |  | 
Set B
7 |  |  |  |  | 
way 1
way 4
12 | 13 | 14 | 15 | 16 | 

## Slide 7: Final Effect
All uops fit in DSB in the fast case
Slow case flip flops in and out of DSB->mite
  Penalties associated with this
Fast case hits LSD for maximum throughput
Slow case becomes FE bound
Significant performance swings (50% - 70%)

## Slide 8: What Can/Shall We Do?
Pad dead space after JMPs when we see multiple JMPs in a 32B chunk
  Example: Adding “.align 32” after 3rd JMP in a loop gains ~60%
  Con : How often is this an issue? How much will this bloat code? Potential to have negative effects (increase FE footprint, introduce new aliasing, etc)
  Maybe worth a quick prototype to evaluate #cases vs perf gains vs bloat for arch-specific flags
Do Nothing
  Con: Potentially leave performance and stability on the table
  Pro: Avoids bloating code for questionable gains. How long will this be an issue? Could potentially have negative effects in some cases.
Other options?